## Slide 2
History of Hvar double solar telescope
Installed in 1972 based on an agreement between Faculty of Geodesy of the University of Zagreb and the Astronomical Institute of the Czechoslovak Academy of Sciences, Ondrejov.
And from Yugoslav side (Faculty of Geodesy):
Prof. Veljko Petković and later Dr.sc. Vladimir Ruždjak
In establishment of Hvar Observatory from Czechoslovak side were participating (Astronomical Institute, Ondrejov):
Dr. B. Valníček, Dr. V. Bumba, Doc. L. Perek, Ing. V. Rajský, Prof. F. Šorm

## Slide 3: Photographic material aqusition system
1972 – 1997
Ambrož et al., 1977

## Slide 4: Video-recording acquisition system
1997 – 2004
Klvana and Bumba, 1997

## Slide 5: CCD camera aquisition system
2004 – 2010
Otruba, 2005
1MPix 10-bit Pulnix TM-1010 CCD camera
Ha, 28.10.2009

## Slide 6: Double Solar Telescope at Hvar
fourth generation of acquisition hardvare and software
4MPix Pulnix TM-4200GE 12-bit CCD cameras
Identical acqusition system as the Kanzelhöhe Solar Observatory (collaboration with IGAM, Uni Graz)
Allows high-resolution images of active-regions on the Sun
Cadence up to 30 images per minute
New hardware is almost not affected by strong transmitter interferences
All data are stored to central archive on server in Zagreb (oh.geof.unizg.hr)
2010 - today

## Slide 7: Some recent improvements
control room
New acquisition system - 2010
Photospheric telescope:
  Baader AstroSolar film (ND 3.8) was introduced instead of prism (reduced telescope heating)
  Simplified and improved optical design
  Baader solar continuum and UV/IR filter were added
Mechanical tracking error significantly reduced by adjusting the telescope mount axes
New tracking motors
Electronic system for computerized tracking and control of the telescope (not yet fully operational)
Better internet connection (50Mbps)

## Slide 8: Photospheric telescope
Main objective (acromatic doublet) with diameter of 217mm and focal lenght of 2450mm
Field of view: 11.3 arcmin
Resolution of 0.33 arcsec/pixel (2048x2048 CCD), oversampled images (1 arcsec for best seeing conditions)
Cadence: 1 image per minute

## Slide 9: Cromospheric telescope
Main objective (acromatic doublet) with diameter of 130mm and focal lenght of 1950mm
Baader research grade filter (656nm) with passband 0.2Å
Field of view: 7.15 arcmin
Resolution of 0.21 arcsec/pixel (2048x2048 CCD), oversampled images
Cadence: 4 images per minute

## Slide 10: Observations in white light
23.9.2011 08:52 UT
27.9.2011 11:40 UT
28.9.2011 08:03 UT
29.9.2011 06:44 UT
30.9.2011 10:19 UT
03.10.2011 07:39 UT
Sunspot group: 11302
Notes: 8919 slika…

## Slide 11: Observations in Ha
Processed image
04.07.2012, 11:55 UTC
Sunspot group: 1515

## Slide 12: Observations in Ha
22. September 2011, sunspot group 11302, X1.4 flare
07:45:45 UT
07:57:32 UT
08:52:25 UT

## Slide 13: Some common artifacts at Hvar
27.10.2013, 12:02 UTC

## Slide 14: Some stats about observations
Hα observations (cadence 15 sec):
  Number of days observing: 321
  Number of images: 320 500
  Total duration: 1335h (55 days)
  Size in archive: 2.6 Tb
WL observations (cadence 60 sec):
  Number of days observing: 303
  Number of images: 74 500
  Total duration: 1241h (51 days)
  Size in archive: 600 Gb
6.5.2011 - 17.09.2014
Chart: 
 | 321 | 1230

## Slide 15: Distribution of observations 2011-2013
Chart: 2011
Chart: 2012
Chart: 2013
Chart: 2014
| 41695.0 | 41696.0 | 41698.0 | 41710.0 | 41711.0 | 41712.0 | 41715.0 | 41716.0 | 41739.0 | 41765.0 | 41768.0 | 41781.0 | 41787.0 | 41794.0 | 41795.0 | 41796.0 | 41799.0 | 41800.0 | 41801.0 | 41802.0 | 41803.0 | 41810.0 | 41822.0 | 41823.0 | 41824.0 | 41826.0 | 41827.0 | 41829.0 | 41843.0 | 41844.0 | 41845.0 | 41852.0 | 41857.0 | 41858.0 | 41863.0 | 41869.0 | 41870.0 | 41876.0 | 41879.0 | 41886.0 | 41889.0 | 41890.0 | 41891.0 | 41892.0 | 41894.0 | 41897.0 | 41898.0 | 41899.0
 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 16: Some planned improvements on Hvar Solar Telescope
Fully computerized tracking system
Reconstruction of solar telescope dome
Improvment of data post-processing
Completion of web page interface to retrieve the data
Weather station (winter 2014/2015)

## Slide 17: Thank you!
Data archive and more information about Hvar Solar Telescope:
http://oh.geof.unizg.hr/index.php/en/instruments/solar-telescope
Notes: Zahvala Niksa Novak
Grad Hvar….
Katica Vucetic…